## Slide 1: Computer Vision for Autonomous Driving and Intelligent Transportation
ITA0502- Computer Vision
Team- 1
Presented by:
Mallela shashanka(192311083)
K.Sathish (192311084)
Konanki Harshini Sriya(192421283)
R.Pavithra(192421369)
Siddartha Achari(192425047)
Guided By
Dr. R C Jeni Gracia
Notes: PRESENTER 1. Welcome and goal: show how a car turns camera images into safe driving decisions. Team split: P1 slides 1-2, P2 slides 3-4, P3 slides 5-6, P4 slides 7-8, P5 slides 9-10.

## Slide 2: Overview: five building blocks
a
Image preprocessing and road/lane segmentation
finds the drivable path
b
YOLO object detection
finds vehicles, pedestrians, signs, obstacles
c
Optical flow and tracking
estimates how objects move
d
Stereo vision
estimates depth, distance and 3D
e
Scene understanding and decision-making
navigation and collision avoidance
Notes: PRESENTER 1. Walk through the five modules. Each output feeds the next one. Everything must run in real time on onboard hardware.

## Slide 3: (a) Preprocessing and lane segmentation
Capture frames from the front camera
Preprocess: undistort, resize, denoise, boost contrast (CLAHE)
Segment pixels into road, lane and background
Fit lane curves to get the drivable path
Methods
Classical: Canny edges + Hough lines
Deep learning: U-Net, DeepLab
Metric
mIoU
Output
Lane lines + drivable-area mask
Notes: PRESENTER 2. Camera frames are cleaned (undistort, denoise, contrast), then each pixel is classified as road or lane. Classical methods are fast but fragile in shadows; deep segmentation is more robust. The lane curve defines the path the planner follows.

## Slide 4: (b) YOLO-based object detection
YOLO predicts boxes and classes in one forward pass
Detects vehicles, pedestrians, traffic signs and obstacles
Non-maximum suppression (NMS) removes duplicate boxes
Fast enough for real-time use on an onboard GPU
Metrics
IoU, mAP, FPS, latency
Datasets
KITTI, BDD100K, COCO
Output
Box + class + confidence score
Notes: PRESENTER 2. YOLO predicts boxes and classes in a single forward pass, so it is fast enough for real time. Non-maximum suppression removes duplicate boxes. Mention small distant objects and night/rain as hard cases.

## Slide 5: (c) Optical flow and object tracking
Optical flow estimates pixel motion between frames
Tracking keeps the same ID for each object over time
Kalman filter predicts the next position
Hungarian algorithm matches detections to tracks
Ix·u + Iy·v + It = 0
Flow methods
Lucas-Kanade (sparse)
Farnebäck (dense)
RAFT (deep)
Trackers
SORT, DeepSORT, ByteTrack
Output
Speed and direction
Notes: PRESENTER 3. Optical flow gives per-pixel motion using brightness constancy. Tracking links detections over time: Kalman filter predicts, Hungarian algorithm matches. Result: speed and direction of each object.

## Slide 6: (d) Stereo vision: depth and 3D
Two cameras see the same point at different positions
The shift between them is the disparity (d)
Pipeline: rectify, match, disparity map, depth, 3D points
Depth error grows with distance
Z = f · B / d
Where
f = focal length (px)
B = baseline (m)
d = disparity (px)
Matching
SGBM or deep (PSMNet)
Output
Depth map + 3D point cloud
Notes: PRESENTER 3. Two cameras with a known baseline see a point at different positions; the shift is disparity. Depth Z = f*B/d. Steps: rectify, match, disparity map, depth, point cloud. Error grows with distance squared, so far objects are less accurate.

## Slide 7: (e) Scene understanding with deep learning
Combine segmentation, detection and depth into one scene model
Bird's-eye-view (BEV) map fuses all cameras
Multi-task networks share one backbone to save compute
Predict future paths of pedestrians and vehicles
Models
Panoptic segmentation
BEVFormer
Trajectory prediction
Output
Scene map + predicted paths
Notes: PRESENTER 4. Combine segmentation, detection and depth into one scene model. BEV models give a top-down map; multi-task networks share a backbone to save compute; prediction forecasts where others will go.

## Slide 8: Decision-making and collision avoidance
Loop: perception → prediction → planning → control
Compute time-to-collision (TTC) for every tracked object
Warn, brake or steer when TTC is below a threshold
Planners: rules, model predictive control, learned policies
Optimize models (TensorRT, quantization) for real time
TTC = distance / v_rel
Real-time target
About 100 ms end-to-end (typical)
Safety
Fail-safe fallback if perception fails
Notes: PRESENTER 4. Loop: perception, prediction, planning, control, many times per second. Time-to-collision is distance divided by closing speed; brake or steer when it drops below a threshold. The 100 ms figure is a typical design target, not a standard.

## Slide 9: ITS applications and open challenges
ITS applications
Traffic monitoring and signal control
Incident and wrong-way detection
License plate recognition
V2X cooperative perception
Driver monitoring
Open challenges
Night, rain, fog and glare
Occlusion in crowded scenes
Domain shift across cities
Rare edge cases
Safety validation and explainability
Notes: PRESENTER 5. The same vision stack supports traffic monitoring, incident detection, plate recognition, V2X and driver monitoring. Challenges: weather, occlusion, domain shift, rare cases, safety validation.

## Slide 10: Conclusion
Segmentation finds the drivable path
YOLO detects objects in real time
Optical flow and tracking estimate motion
Stereo vision gives depth and 3D
Scene understanding supports safe navigation
Future work
Camera + LiDAR + radar fusion
Transformer / BEV models
V2X cooperation
Verified safety
Thank you
Notes: PRESENTER 5. Recap the five modules and how they form one pipeline. Future work: sensor fusion, transformer/BEV models, V2X, safety validation. Invite questions; route them to the relevant presenter.